## Slide 1: suture selection

## Slide 2: Suture selection
Principles of wound closure
Suture sizes
Suture types
  Mono-filament vs multi-filament
  Absorbable vs non-absorbable
Needle types
Selecting the right suture

## Slide 3: Principles of wound closure
You only need suture around for as long as it takes for tissue to regain its tensile strength (ie until the tissue can withstand its usual stress without additional support)
Goal-create optimal healing in minimal time and minimize the risk of infection
http://www.uphs.upenn.edu/surgery/Education/facilities/measey/Wound_Closure_Manual.pdf

## Slide 4: Suture sizes
Size denotes diameter
Stated numerically (as number of 0’s increases, diameter decreases)
  0, 2-0, 5-0
The smaller the size, the less tensile strength
Use the smallest size that will have adequate tensile strength for that tissue minimizes the amount of foreign body left in the patient

## Slide 5: Suture types
Mono-filament | Multi-filament
Single strand | Several strands braided together
Less resistance through tissue | Greater tensile strength, pliability, flexibility
Less infection (resist harboring organisms) | 
Tie down easily | 

## Slide 6: Absorbable vs Non-absorbable
Classified by degredation properties
Absorbable
  lose tensile strength within 60 days
  May be treated or chemically structured to lengthen absorption time
  Natural sutures-digested by body enzymes
  Synthetics-hydrolyzed, lesser tissue reaction
  May accelerate in presence of fever/infection
Non-absorbable-retain tensile strength >60 days
  Encapsulated by fibroblasts
  Remain permanently
  May be preferred in patients with reaction to absorbable suture, keloid, or hypertrophic scarring

## Slide 8: Barbed sutures
V-loc
  Dual angle barb
  Preformed loop
  More difficult/impossible to remove
  90 vs 180 day closure
Stratafix
  Single angle barb
  Adjustable loop
  Can overcome barb to readjust slightly
  90 vs 180 day closure

## Slide 10: Lapra-ty
Only approved for Vicryl, sizes 2-0, 3-0, 4-0 and 2-0 PDS

## Slide 11: Suture selection
When a wound reaches maximal strength, suture is no longer needed
Tissues that heal slowly (skin, fascia, tendons)-close with non-absorbable suture or absorbable sutures with extended wound support
Those that heal rapidly (stomach, colon, bladder)-may be closed with absorbable suture
Foreign bodies in potentially contaminated tissues may convert contamination to infection
When cosmesis is important, close and prolonged apposition of wound edges produces best results
  Use smallest inert suture, close subcuticular, skin adhesive or tape may aid is apposition
Foreign bodies in presence of high concentrations of crystalloids my act as a nidus for stone formation (ie bladder)-use rapidly absorbed sutures

## Slide 12: Suture selection
Fascia
  Prolene
  PDS/Maxon
Subcutaneous fat
  Vicryl/Polysorb
Subcuticular
  Chromic
  Monocryl
Skin
  Vicryl Rapide
  Monocryl
Drains, retention sutures
  Ethibond

## Slide 13: Needle types
Swaged on vs pop-off

## Slide 14: Needle types
Needle shape
  Taper
    Typically used in tissue that is easy penetrated
  Cutting
    Used in difficult to penetrate tissues (fascia, skin,
  Reverse cutting
Attachment
  Swaged on
  Control release (ie pop off)
Notes: Conventional cutting-may cut out a portion of tissue given design
Reverse cutting-for difficult to penetrate tissues (skin, tendon), more strength than conventional needle, less danger of cut out