## Slide 1: Instruments: laparoscopic and Robotic surgery

## Slide 2: Telescope
Laparoscopes
  Various sizes
    2-3mm needlescopes
    5mm
    10mm
  Visualization capabilities
    0 degree
    30 degree
    45 degree
Hysteroscopes
  0 degree
  12.5 degree
  30 degree
Cystoscopes
  30 degree
  70 degree

## Slide 3: Light source

## Slide 4: CO2 insufflator

## Slide 5: Instruments: Laparoscopic surgery

## Slide 6: Instruments: Energy sources

## Slide 7: Energy types
  Ligasure
  Enseal
  Gyrus ACMI
  Harmonic
Combination
  Thunderbeat

## Slide 8: Energy types
Monopolar
Active electrode within surgical wound
Return electrode elsewhere on patient (typically thigh)
Current must flow through the patient to the return electrode to complete the circuit
Bipolar
Both active and return electrode functions are in the surgical wound
Two tines of the forceps perform the functions of the active and return electrodes
Only the tissue grasped is included in the electrical circuit

## Slide 9: Tissue Effects
ENERGY SOURCE | TISSUE EFFECTS
Monopolar electrosurgery | Vaporisation, fulguration, desiccation, coaptation*
Conventional bipolar electrosurgery | Desiccation, coaptation
Advanced bipolar electrosurgery** | Desiccation, coaptation, blade tissue transection
Ultrasonic technology | Desiccation, coaptation, mechanical tissue transection
Vessel sealing achieved with coagulation and compression.**Tissue impedance monitoring optimizes activation time

## Slide 10: Monopolar

## Slide 11: Bipolar

## Slide 12: Advanced Bipolar Energy
Ligasure (Covidien)
Enseal (Ethicon)
Gyrus ACMI (Olympus)

## Slide 13: Advanced Bipolar-Ligasure
https://www.youtube.com/watch?v=26cMx8LWk_A
Combination of pressure and energy leading to denaturation of collagen and elastin creating a permanent seal
Hydrothermal rupture of collage crosslinks
Adjusts energy levels according to tissue impedance
Permanently fuses tissue and vessels without dessication
Seals up to 7mm, withstands up to 3 times systolic pressure

## Slide 14: Advanced Bipolar-Enseal
Adjusts energy based on impedance
Nanotechnology adjusts and shuts off current when temperature reaches a set pointminimizes thermal spread
Vessels sealed with compression, protein denaturation and renaturation
Seals up to 7mm, withstands up to 7x systolic BP
1 mm thermal spread
https://www.youtube.com/watch?v=Nj9NLkZmliM
Notes: Enseal
Uses a nanotechnology feedback system which adjusts the temperature by feedback from the device
minimizes thermal spread
Seals up to

## Slide 15: Advanced bipolar-gyrus acmi
Plasma kinetic energy, delivered impulses
Forms vapor zones which collapses causing tissue sealing
Intermittent tissue cooling (prevents thermal damage and sticking)
Audible impedance and end point indicator
Notes: Gyrus ACMI

## Slide 16: Ultrasonic Scalpel
Converts ultrasonic to mechanical energy, 55000 vibrations/sec
Lysis of H bondsheatdenaturation of proteinseparation of tissue
Simultaneous cutting and coagulation
Seals vessels up to 5mm (up to 7mm with ACE7)
BENEFITS: greater precision in tight spaces near vital structures, less char, less smoke
https://www.youtube.com/watch?v=1SFUjk7nSqI

## Slide 17: Hybrid energy-thunderbeat
Combination of advanced bipolar and ultrasonic energy
Seals vessels up to 7mm
https://www.youtube.com/watch?v=20eSwDHrjIg

## Slide 18: Energy sources

## Slide 20: Cost comparison

## Slide 21: Laparoscopic Suture devices
EndoLoop

## Slide 22: Laparoscopic clip applier
Ligate blood vessels and other tubular structures
Titanium or absorbable
Hemo-lock
Clip applier
Bulldog clamp

## Slide 23: Staplers
More commonly used in general surgery
  Bowel transection/anastomosis
  Appendectomy
Range of loads corresponding to staple height
Blue = bowel

## Slide 24: Uterine Manipulators
Notes: he slightly curved shanks and tips provide the user a better view when suturing intravaginally,

## Slide 25: Basic
Hulka
Rubin/Cohen/Acorn

## Slide 26: Humi
Modified endotracheal tube
Cheap
Disposable

## Slide 27: Clear view
Uterine manipulator and injector
Balloon seal for chromopertubation
Can perform all manipulations with patient in supine position
https://www.youtube.com/watch?v=NCZRfDMA7AE

## Slide 28: Colpotomy cups
Normal relationship of ureter to fornix and uterine artery
Pushing up with cup after vesicouterine peritoneum divided. Distance between fornix and ureter has increased

## Slide 29: V-Care
Single use device
Variable sized colpotomy cups (Harmonic compatible)
Back cup designed to limit loss of pneumo
  Variable success
  Can use separate Colpo-Pneumo-Occluder
May not work well for very large uteri
Vcare Dx-Can perform chromopertubation (not an option in regular Vcare)
VCare and VCare Dx
    https://www.youtube.com/watch?v=mOp4mmEnH18
    https://www.youtube.com/watch?v=nRqQ8ClfEXE

## Slide 30: RUMI
Reusable hand piece
Variable length tips
Koh rings in variable sizes, materials (plastic or stainless steel)
Colpo-Pneumo-Occluder-prevents loss of pneumoperitoneum
More difficult to put together and place, particularly in narrow vaginas
    https://www.youtube.com/watch?v=YSDUNXI_EAs
    https://www.youtube.com/watch?v=VMB42641H9I

## Slide 31: RUMI ARCH
Reusable hand piece
Similar tips to RUMI, variable KOH ring sizes
Attached Colpo-Pneumo-Occluder balloon

## Slide 32: Advincula delineator
Disposable
Integrated Koh cup
  Plastic, steel, flexible soft
Intrauterine tip within device-adjustable

## Slide 33: Fornisee
Illuminated cup delineates fornices
Reusable uterine sound/tip
Multiple sizes
Baffled vaginal occlude built in to maintain pneumoperitoneum

## Slide 34: Cost comparison

## Slide 35: Trocars
Notes: he slightly curved shanks and tips provide the user a better view when suturing intravaginally,

## Slide 36: types
Cutting
  Shielded
  Non-shielded
Blunt

## Slide 37: Versastep system
Combines a nylon stretchable sheath over a disposable Veress needle
Sheath then dilated with a blunt conical dilator
May create a smaller fascial defect with less need for closure

## Slide 38: Single site/multiport systems

## Slide 39: Cost comparison

## Slide 40: SILS surgery

## Slide 41: Cheap variety

## Slide 42: Specimen retrieval bags
EndoPouch
Anchor
Genistrong (reusable)
Alexis containment system

## Slide 43: Instruments: Robotic surgery
Notes: he slightly curved shanks and tips provide the user a better view when suturing intravaginally,

## Slide 44: robotic surgery
High grasp strength
High grasp strength
High grasp strength
Low grasp strength
Low grasp strength